## National 4 Music Technology Skills

### Sample Unit assessment brief 4 — applying EQ and reverb to an acoustic guitar

Your task is to EQ a previously recorded acoustic guitar track, following the brief below.

You may be guided through these steps by your assessor.

Applying EQ

Open the acoustic guitar session within your recording software or hardware.

Add an EQ plug in to the acoustic guitar track.

Set a high pass filter to around 150 Hz.

Adjust the frequency up and down until you hear the guitar sound full but not too ‘boomy’.

Boost some high mid frequencies (between around 4 kHz to 7 kHz) by up to 
4 db.

Applying reverb

Add a reverb plug in to your acoustic guitar track.

Choose a room reverb.

Adjust the dry/wet balance until you hear a good balance of dry signal and effected sound.

Readjust your EQ boost to balance well with the reverb. You may find that you need less of a boost.

Update your log.