## Music Technology Skills (National 5)

### Sample Unit assessment brief 3 — acoustic guitar task

Your task is to record an acoustic guitar, using a coincident XY stereo micing technique. Follow the brief below.

Open an existing session within your recording software or hardware, or setup a new session if required.

Add two audio tracks.

Set up one mic stand if using a stereo bar. If you don’t have a stereo bar, set up two mic stands.

Attach small diaphragm cardioid condenser mics to the stand(s). (SDCs are good choices but are not the only choices for this application.)

Fix the mics so that the capsules are at a 90۠° to one another. This can be arranged with the capsules nearly touching or with the mics one on top of the other.

Attach cables, following appropriate safety procedures.

Tune instrument.

Adjust gain as the performer plays/sings to a suitable level for recording.

Wearing headphones, adjust the mic positions as your performer plays.

Adjust the headphone monitoring volume to a level that is appropriate for the performer.

Record the instrument.

Update your log.

Note that you can adapt this brief to cover stereo micing of small ensembles. You may also explore other stereo technique such as ORTF.