## Music Technology Skills (National 5)

### Sample Unit assessment brief 5 — mix

Your task is to apply a range of mixing skills to a multi-track session consisting of at least five parts, following the brief below. You must include at least one insert effect and one effects send, and use EQ and dynamics as appropriate.

Open the session and name it as your own, saving into your folder.

Open the mix window.

Listen to the track and roughly balance the parts using the faders, keeping as close to 0 db (but not above) as you can.

Listen again and decide where in the stereo field you want to hear each element, and complete the panning.

Listen again and readjust the balance, using the faders if necessary.

Apply EQ and dynamics processing to the parts that require it.

Rebalance the mix as you work through the parts.

Decide which parts you will use effects on and what types of effects. You must decide which are to be sends and which should be inserts.

Apply your effects, both inserts and sends.

Balance the send effects with the dry tracks within the mix. If it is a mono effect, consider panning.

Listen to the whole mix again and adjust the panning/balance if required.

Apply automation to mix elements as appropriate.

Apply EQ/dynamics/effects to the master fader if required.

Bounce down your work to an audio master.

Update your log.